## Slide 1: Services
FW Update and Download
February 2014
Herwig Jahn
Roland Stumpf
Michael Harnischfeger

## Slide 2
Version | Date | Author | Changes
V01 | 26.02.2014 | M. Harnischfeger | First draft
Version History
Document

## Slide 3
Services
How are the Services structured
There are two types of services
  Architecture Layers, shows the structure of the service definition
FTP (S)
Modbus TCP
EtherNet / IP
Services
Protocol
Mapping
Protocol
Mapping
Protocol
Mapping
TCP / IP
High Level Services
Low Level Services
Mapping
Transport
USB
LAYERS
MSU
UDP/IP
UART, USB , CAN...
Protocol
Mapping

## Slide 4
Services
What Services are defined
There are several groups of services defined
  Connection Services, to manage the connection between a loading tool and the device including security aspects (Authorization, etc.)
  Information Services, to get more details about the device, its capabilities and restrictions.
  Loading Services, to download and upload data or files as well as preparing the loading.
  A further part is to send commands to initiate a action
  Notification Services, is used to send information to the device on which it can react (optional).

## Slide 5
Services
Connection Services
They are used for setting up a connection to a target system
  Connect, set up the connection and prepare the connection to the target system
  Disconnect, close the connection to the target system
  Security Aspects, this can include different topics depending on the used protocol and target system.
  Authorization  user login when it is required by the target system
      Cryptography  Set up a secure channel for the communication when it is required by the
      protocol or target system
Request
Response
Result / Status
Session ID
User Credentials
Session ID
It is used to identify the connection and to avoid repeating the user credentials every time
Request
Response
Result / Status
Session ID

## Slide 6
Services
Information Services
They are used to identify and check capabilities and limitations of a target system
  Get Device Information, retrieves static information about a target system
  Get Device Status, retrieves dynamic information about a target system
Request
Response
Device Info
Firmware Info
Session ID
Filter
Routing Info
…
Can be extended by Application info, etc
Modules, Components, Sub Target Information
Installed firmware, supported loading mode, etc
Identification and communication capabilities
Filter can be used to retrieve only the interesting information of the device
e.g. to retrieve only firmware information
Request
Response
Device State
Memory State
Session ID
Filter
Error State
…
Can be extended by custom status information
Get error information of the target system
How much space is free
In which state is the device: RUN, STOP, etc
Filter can be used to retrieve only the interesting information of the device
e.g. to retrieve only the state in which the device is “RUN”

## Slide 7
Services
Loading Services
The group is again split in to section. The first part is about exchanging the packages.
  Download Package, transfers the package from a tool to a target system
  Upload Package, transfers a package from a target system to a tool
Request
Response
Result / Status
Session ID
Package
Request
Response
Result / Status
Session ID
Object ID
Package
Refers to a object/ package which should be return from the target system

## Slide 8
Services
Loading Services
The second part is about initiating actions on target system side and retrieving loading information
  Prepare Loading, send metadata for matching check as well as bring the target system to install mode
  Send Command, send a command to initiate a action on the target system
  Get Loading Status, retrieves the status / progress during the loading process
Request
Response
Result / Status
Session ID
Command
Parameter
Install FW
Name=Location; Value=SD Card
Request
Response
Action
Session ID
Status / Progress
Message
Parameter
Object ID when send command to create backup
CPU = BUSY; Progress = 80%
File A installed
Request
Response
Result / Status
Session ID
Package Metadata

## Slide 9
Services
Notification Services
They are used to inform a target system about events so that a system can react
  Send Notification, inform the target about an event e.g. new firmware update available
Request
Response
Result / Status
Notification
Info Type
Parameter
FW update available
Name=Location; Value=ftp:\\...

## Slide 10
Services
The Communication in details
The point of view from the high level services (example: Cached Loading)
Tool
Device
Download Package
Generate Session ID
Get Loading Status
Connect
Authorization check
:Result
:Result
:Result
Get Device Information
:Result
Prepare Loading
:Result
Session ID
Filter
Device Information
Session ID
Credentials
Send Command
:Result
Session ID
Session ID
Metadata
Session ID
Package
Session ID
Command: INSTALL
Progress
Matching check
Select Loading
Mechanism & Mode
Start Loading Mode
Store Package
Analyze Metadata
& Check matching
Install FW data
Cyclically called
until COMPLETE
End
Progress
Status: COMPLETE

## Slide 11
Services
What about the Protocol Mapping
Layer view in the tool and device implementation
Tool
Device
Transport Protocol: Modbus TCP
API
High level Services
Mapping
To Modbus TCP
Protocol Stack
Modbus TCP
Mapping
From Modbus TCP
Protocol Stack
Modbus TCP
Callback
Objects /
Registers
FW Installer
Platform specific
Switch:
Via Function Code (FC)

## Slide 12
Services
What’s behind Protocol Mapping
Sequence of the mapping to Modbus
Stack
Device
Get Device Information
Modbus Request Message
API
(High Level Services)
Mapping
Session ID
Filter
Response Data
Session ID
Filter
Checks Format
Objects or XML file
 Process input
Request Data
Func. Code
Modbus Frame
Service Code
Request
Data
Func. Code
Modbus Frame
Response
Data
Modbus Response Message
Status Code
Process data from
Objects or XML file
 Process input
Return
Device Info
Device Information
Device Information